## Slide 1
Organized by:
National Reconstruction Authority(NRA)
MOUD/District Project Implementation Unit (DLPIU)
Housing Recovery and Reconstruction Platform-Nepal (HRRP)
Housing Recovery and Reconstruction Platform-Nepal (HRRP) Orientation Program for Partner organizations
on
Dry Stone Masonry Construction

## Slide 2: Why Dry Stone Masonry ?
This Type of Construction Common in Northern Area of Nepal
In Northern Parts People don’t Prefer Mud mortar
it is difficult to transport cement and steel since these sites are very remote and have no road access
Many Dry Stone Masonry Houses are already under Construction

## Slide 3: Dry Stone Building Practices
.
Extensive longitudinal walls and open front

## Slide 4: Dry Stone Building Practices
Stand alone, most with open fronts

## Slide 5: Dry Stone Building Practices
Dry Stone masonry or Stone in mud buildings with heavy Stone roofs
Presence of corner stones

## Slide 6: Dry Stone Building Practices
No other Earthquake Resisting Element

## Slide 7: Dry Stone Building Practices
Steep Gable

## Slide 8: Dry Stone Building Practices
No proper connection of ridge beam, rafter and bottom chord
No proper connection of roof elements with wall

## Slide 9: Dry Stone Building Practices
Dry Stone masonry with light CGI sheets
No earthquake resisting elements
Presence of corner stones
Use Gable wall
New Construction after Earthquake

## Slide 10: Dry Stone Building Practices
Timber walls at the front part and inner side of all stone walls
Many Buildings!
New Construction after Earthquake

## Slide 11: Dry Stone Construction-Deficiencies
Gable End Wall Damage
Heavy masonry gable walls are unsupported and subject to lateral loads from roof.

## Slide 12: Dry Stone Construction-Deficiencies
Short Wall Out-Of-Plane
Weak attachment between end walls and diaphragms.
Damage to and subsequent collapse of end walls due to out-of-plane demands.
Wooden slab diaphragm unable to transfer Earthquake force Properly.

## Slide 13: Dry Stone Construction-Deficiencies
Wall Delamination in both directions
The thick walls (>=45cm) constructed of interior and exterior facing stones. Required bonding elements are sometimes missing or inadequate.
Wall delamination occurs, can lead to subsequent collapse.

## Slide 14: Type Design On Dry Stone Masonry
Dressed Stone Masonry
Random Rubble Masonry with GI Wire Mesh

## Slide 15: Dressed Stone Masonry
No. of Storey : 2
Flexible Floor & Roof
Plinth Area: 588 sq.ft

## Slide 16: Dressed Stone Masonry
Foundation
Width: 900 mm
Depth : 900 mm

## Slide 17: Dressed Stone Masonry
Provide Horizontal Band at Plinth, Sill , Lintel &Roof level
Well Seasoned Locally available hardwood can be used

## Slide 18: Dressed Stone Masonry
Wall Thickness : 600mm
Spacing of through stone should not be more than more than 1200 mm horizontally & 600 mm Vertically
Provide Vertical Member at Corner of Wall

## Slide 19: Vertical Member Detailing

## Slide 20: Roof Detailing
In timber connection it need give Special attention in Joint !

## Slide 21: Wooden Key

## Slide 22: Random Rubble Masonry with GI wire Mesh
No. of Storey : 2
Flexible Floor & Roof
Plinth Area: 588 sq.ft

## Slide 23: Random Rubble Masonry with GI wire Mesh
Foundation
Width: 900 mm
Depth : 900 mm

## Slide 24: Random Rubble Masonry with GI wire Mesh
Wall Thickness : 600mm
Spacing of through stone should not be more than more than 1200 mm horizontally & 600 mm Vertically

## Slide 25: Random Rubble Masonry with GI wire Mesh
The hot dipped galvanized welded wire Shall be used to ensure the Corrosion Protection
The wire mesh shall not be less than 50 Micron

## Slide 26: Roof Detailing
In timber connection it need give Special attention in Joint !

## Slide 27: Wooden Key

## Slide 28: Random Rubble Masonry with GI wire Mesh
The hot dipped galvanized welded wire Shall be used to ensure the Corrosion Protection
The wire mesh shall not be less than 50 Micron

## Slide 29
Even with the low compliance rate
We can
still Considered it as a good Initiation !

## Slide 30: Tipling, Dhading

## Slide 31: Ramche, Rasuwa

## Slide 32: Sertung, Dhading

## Slide 33: Dhading

## Slide 34
Thank You